Registered with the Ministry of Justice of Russia on July 6, 2018 under Reg. No. 51547

RUSSIAN FEDERATION MINISTRY OF TRANSPORT

(MINTRANS OF RUSSIA)

ORDER

No. 173 of May 4, 2018

ON APPROVAL OF OKHOTSK SEAPORT REGULATIONS

# Pursuant to Article 14 of Federal Law No. 261-FZ of November 8, 2007 On Seaports in the Russian Federation and On Amendments to Certain Legislative Enactments of the Russian Federation (Collected Statutes of the Russian Federation, 2007,  No. 46, Art. 5557; 2008, No. 29, Art. 3418, No. 30, Art. 3616; 2009, No. 52, Art.  6427; 2010, No. 19, Art. 2291, No. 48, Art. 6246; 2011, No. 1, Art. 3, No. 13, Art. 1688, No. 17, Art. 2313, No. 30, Art. 4590, Art. 4594; 2012, No. 26, Art. 3446; 2013, No. 27, Art. 3477, No. 30, Art. 4058; 2014, No. 45, Art. 6153, No. 49, Art. 6928; 2015, No. 1, Art. 52; No. 29, Art. 4339; 2016, No. 27; Art. 4215; 2017, No. 27, Art. 3945, No. 30, Art. 4457) <*>,

IT IS HEREBY ORDERED TO:

------------------------------------

<*> 2018, No. 1, Art. 34, 44.

Approve of the Okhotsk Seaport Regulations attached.

Minister:

M.Yu. Sokolov

# Approved by:

Mintrans of Russia Order No. 173

of May 4, 2018

OKHOTSK SEAPORT REGULATIONS

## I. General Provisions

1. 	Okhotsk Seaport Regulations (hereinafter: the Regulations) have been developed in conformity with Federal Law No. 261-FZ of November 8, 2007 On Seaports in the Russian Federation and On Amendments to Certain Legislative Enactments of the Russian Federation, Federal Law No. 81-FZ of April 30, 1999 Merchant Shipping Code of the Russian Federation <1>, General Rules of Ship Navigation and Anchorage in Seaports of the Russian Federation and Approaches Thereto <2> (hereinafter: the General Rules.

--------------------------------

<1> Collected Statutes of the Russian Federation, 1999, No. 18, Art. 2207; 2001, No. 22, Art. 2125; 2003, No. 27, Art. 2700; 2004, No. 15, Art. 1519, No. 45, Art. 4377; 2005, No.   52, Art. 5581; 2006, No.  50, Art. 5279; 2007, No.  46, Art. 5557, No.  50, Art. 6246; 2008, No.  29, Art. 3418, No.  30, Art. 3616, No.  49, Art. 5748; 2009, No.  1, Art. 30, No.  29, Art. 3625; 2010, No.  27, Art. 3425, No.  48, Art. 6246; 2011, No.  23, Art. 3253, No.  25, Art. 3534, No.  30, Art. 4590, 4596, No.  45, Art. 6335, No.  48, Art. 6728; 2012, No.  18, Art. 2128, No.  25, Art. 3268, No.  31, Art. 4321; 2013, No.  30, Art. 4058; 2014, No.  6, Art. 566, No.  42, Art. 5615, No.  48, Art. 6659; 2015, No.  1, Art. 89, No.  13, Art. 1810, No.  29, Art. 4339, 4356; 2016, No.  27, Art. 4186, Art. 4215, 2017, No.  7, Art. 1029, No.  27, Art. 3945, No.  30, Art. 4457, No.  52, Art. 7293; 2018, No.  1, Art. 44.

<2> Mintrans of Russia Order No. 463 issued October 26, 2017 On Approval of General Rules of Ship Navigation and Anchorage in Seaports of the Russian Federation and Approaches Thereto (registered with the Ministry of Justice of Russia on March 23, 2018, Registration No. 50497).

2. 	These Regulations include the description of Okhotsk seaport (hereinafter: the Seaport); rules of seaport entry and seaport exit, including measures of navigational safety for ships to enter/exit the seaport; rules of navigation within the seaport waters and approaches thereto; description of the area covered by a ship traffic management system and rules of ship navigation therein; rules of ship stay in the seaport and anchorage ground arrangement; rules of ecological safety, including identification of shipboard waste to be collected at the seaport, and rules of quarantine compliance in the seaport; rules to use special communication facilities within the seaport territory; data on seaport limits; data on approaches to the seaport; data on the seaport capability to accommodate ships; data on a navigation period; data on compulsory pilotage areas; data on water depths in the seaport and on approaches thereto; data on hazardous cargo handling; data on transmission of information by masters of the ships staying in the seaport in case of a threatened act of unlawful intervention in the seaport; data on transmission of navigational, hydrological and meteorological information to masters of the ships staying in the seaport; transmission of other information required by the Russian Federation’s regulatory acts in the field of merchant shipping.

3.	These Regulations shall be binding on all ships irrespective of their national and departmental identity as well as all individuals and legal entities, operating in the seaport.

4.	Ship navigation within the seaport and approaches thereto, ship stay in the seaport waters shall comply with the General Rules and the present Regulations.

## II. Seaport Description

- 5. 	The seaport is located in the northern portion of the Sea of Okhotsk in a lagoon at the mouth of Kukhtuy river on the Tungusky spit. The seaport has a cargo multilateral border checkpoint <3>. The seaport is referred to as a freezing port, icebreaker assistance in the seaport is not provided.

--------------------------------

<3> Russian Federation Government Decree No. 2665-р of November 28, 2017 (Collected Statutes of the Russian Federation, 2017, No. 49, Art. 7527).

6. 	The seaport limits were approved of by the Russian Federation Government Decree No. 117-р of January 29, 2015 <4>.

--------------------------------

<4> Collected Statutes of the Russian Federation, 2015, No. 6, Art. 989.

7. 	Data on the approaches to the seaport are provided in Addendum No. 1 hereto.

8. 	Navigation in the seaport begins in June and ends in November.

9. 	Information on the beginning and the end of navigation period shall be provided by the Harbor Master to the seafarers on an annual basis.

10. Navigation within the seaport is carried out under the following hydrological and meteorological conditions:

variable winds in fall and spring;

prevailing south east winds in summer;

storm wind probability: 15%;

the maximum fog frequency: from June through September;

Kukhtuy river flow rate in the entrance channel and berth area makes five knots during tidal rise and ten knots during tidal fall.

An entry to the lagoon at the mouth of Kukhtuy river is located between Okhotskaya Kosa island and the Tungusky spit. There is a sand bar 0.8-1.5 m deep located south of the lagoon entry. Position of the bar varies.

There are wind setups observed at the mouth of Kukhtuy river.

During wind setups:

wave heights reach eight meters;

waves can run over the Tungusky spit and Okhotskaya Kosa island.

Tidal rises and falls at the mouth of Kukhtuy river are semi-diurnal, height of high water makes four meters.

11. 	Fishing nets are set in summer within 0.5 miles south of Okhotskaya Kosa island and the Tungusky spit.

12. 	Tugboat assistance in the seaport shall be compulsory.

13. 	Pilotage in the seaport shall be compulsory. Data on compulsory pilotage area in the seaport are provided in Addendum No. 2 hereto.

14. 	The seaport shall handle cargo, including hazardous cargo.

15. 	Ships in the seaport can be filled up with provisions and fresh water. Ships are not supplied with fuel in the seaport. There are no repair facilities in the seaport.

16. 	Data on very high frequency (hereinafter: VHF) channels used in the seaport are provided in Addendum No. 3 hereto.

17. 	Data on ship anchorage places within the seaport are provided in Addendum No. 4 hereto.

18. 	Data on the seaport capability to accommodate ships and on water depths in the seaport are provided in Chapter IX and Addendum No. 5 hereto.

## III. Seaport Entry and Exit Rules, Including Measures of Navigational

## Safety for Ships to Enter/Exit the Seaport

19. 	Information on the ship calling at the seaport shall be transmitted to the Harbor Master via the Internet site at www.portcall.marinet.ru.

Clearance of ships entering the seaport and exiting from the seaport during the navigation period shall be done on a round-the-clock basis.

20. 	The Harbor Master shall not clear entry/exit of ships, including small crafts, used for commercial purposes which navigate exclusively in the seaport waters or leave the seaport limits and return to the seaport providing that the single voyage duration outside the seaport limits does not exceed 72 hours.

Permission for the aforesaid ships to navigate in the seaport waters and navigate outside the seaport limits with a return to the seaport shall be issued by the Harbor Master for a term of no more than 90 days. The term of permission stated herein may not exceed the term of validity of ship’s papers.

The permission for a ship to navigate in the seaport waters and navigate outside the seaport limits with a return to the seaport shall be issued by the Harbor Master providing that the ship, its crew, hull, machinery and equipment comply with the requirements of international conventions in the field of navigation safety and protection of marine environment against pollution based on the documents provided in  Addenda No. 1 and No. 2 to the General Rules and an application submitted by a shipmaster (shipowner) or  marine agent wherein the following information is provided:

International Maritime Organization (hereinafter: IMO) number of ship (hereinafter: IMO number) (if applicable);

Ship’s name in the Russian language and in Latin characters;

Ship’s call sign;

Maritime Mobile Service Identity of the ship;

Ship owner’s and ship operator’s name and IMO number (if applicable);

Ship’s class (name of organization authorized to class and survey ships that has issued the classification certificate);

Main characteristics of ship (type, year built, gross tonnage, deadweight, overall length, overall width, depth, modulus, extreme draft, draft fore, draft aft, sea area of Global Maritime Distress and Safety System, and permitted navigation area);

nature of ship operations;

navigation area;

any navigation area and season restrictions available;

data on ship security;

information on sanitary and epidemiological situation on board the ship;

information on any problems (if any) with ship-borne cargo handling gear (equipment) as well as ship’s noncompliance with the requirements in the field of safety of life at sea, navigation safety, protection of marine environment against pollution, transport safety.

21. 	The permission for a ship to navigate in the seaport waters and navigate outside the seaport limits with a return to the seaport shall be issued by the Harbor Master in a written form and shall be inclusive of the data stated in the shipmaster’s (shipowner’s) or ship agent’s application and of navigation area and season restrictions placed on the ship as well as permission date and term.

IV. Rules of Navigation within the Seaport Waters and Approaches Thereto

22. 	Ship traffic and ship stay within the seaport waters shall only occur under specific authorization in conformity with berth allotment and traffic schedule (hereinafter: the Daily Schedule). The daily schedule shall be approved by the Harbor Master on a daily basis at or before 17:00 local time based on the ship call information transmitted in the manner provided in Clause 19 hereof.

23. 	Ship traffic within the seaport waters, berthing/unberthing operations and line handling shall be performed upon authorization of the Office of Harbor Master and be controlled by the Office of Harbor Master. The ship shall ask permission to proceed from the Office of Harbor Master.

24. The International Regulations for Preventing Collisions at Sea, 1972 shall be applied to the ship traffic within the seaport waters <5>.

--------------------------------

<5> Collected ongoing treaties, agreements and conventions concluded by the USSR with foreign countries. Iss. XXXIII. - M., 1979, pp. 435 - 461. The Convention came into effect for the USSR on July 15, 1977; the document on the USSR accession to the Convention as amended was deposited with the Secretary General of the Intergovernmental Maritime Consultative Organization on November 9, 1978.

(Official internet-portal of legal information: http://www.pravo.gov.ru, 2016, No. 0001201611240015 with amendments in effect, http://www.pravo.gov.ru, 2016, No. 0001201611240023, No. 0001201611240022, No. 0001201611240021, No. 0001201611240020, No. 0001201611240018).

25. 	Navigation within the seaport waters and Kukhtuy river mouth shall be prohibited under the following weather conditions:

visibility less than four cable lengths;

wind force in excess of 12 meters/second;

wave height in excess of 1.5 meters.

26.	The following ship categories shall be exempted from compulsory pilotage:

small crafts;

pleasure boats;

sport sailers;

crafts engaged in servicing and replenishment of ships in the waters of the seaport and approaches thereto and logistic support of the seaport infrastructure (hereinafter: port fleet vessels).

27. 	Pilots shall embark and disembark from the ships at point at 59°19'18" N and 143°09'00" E and at berths of the seaport given wave heights do not exceed 1.5 meters.

28.	Small crafts, except for port fleet vessels, sport sailers and pleasure boats, shall not be allowed to:

maneuver in the immediate vicinity of ships;

approach the ships lying at anchor or moored alongside the pier;

sail under the wind speed in excess of 12 meters per second;

navigate within anchorage areas;

moor at floating and stationary navigation aids and drop the anchor nearby;

drop the anchor in or near the fairways

approach the berths where hazardous cargo is handled.

29. 	Ships may turn within the seaport waters in the area of berths Nos. 1, 2 and 3.

30. 	While at the mouth of Kukhtuy river, ships having a draft of less than two meters shall give way to ships having a greater draft.

31. 	Overtaking of ships within the seaport waters shall not be allowed.

32. 	Navigation within the seaport waters shall be allowed at the slowest practical speed to hold the ship on course.

33. 	Fairways in the seaport water area are as follows:

main ship channel – along the Kukhtuy river;

lateral in relation to the main channel – exits from the water areas of the former Okhotsk shipyard and Morskoy community.

34.	Ships, except for small crafts, shall not be allowed to navigate in the seaport water area or pass over the sand bar of Kukhtuy river at night.

35. 	Alongside towing over the sand bar of Kukhtuy river shall be prohibited under the following weather conditions:

wind speed in excess of 10 meters per second;

wave height in excess of one meter;

visibility less than four cable’s lengths.

36. 	Towing with a towline not to exceed 30 meters and only one ship at a time as well as alongside towing shall be allowed in the seaport waters.

37. 	Ship towing in the seaport waters shall be allowed under the following weather conditions:

wind speed of no more than 12 meters per second;

wave height of no more than 1.5 meters;

visibility no less than four cable’s lengths.

38. 	Information on the pilotage necessity shall be communicated by the ship in the manner provided in clause 19 hereof and be confirmed two hours before coming to the place of pilot embarkation, the estimated time of unberthing, shifting or exiting the seaport by VHF channels.

V. Description of Area Covered by Ship Traffic Management System

## and Rules of Ship Navigation Therein

39. A ship traffic control and management service (hereinafter: the STCMS) operates in the seaport <6>. The STCMS covers the water area of the seaport and approaches thereto.

--------------------------------

<6> Article 15 (1), Federal Law No. 261-FZ of November 8, 2007 On Seaports in the Russian Federation and On Amendments to Certain Legislative Enactments of the Russian Federation. Mintrans of Russia Order No. 226 of July 23, 2015 On Approval of Requirements to Ship Traffic Radar Control Systems, to Port Infrastructure Facilities Required for Global Maritime Distress and Safety System Operation, to Automated Information System Facilities, to Ship Traffic Control and Management Service (registered with Mintrans of Russia on October 28, 2015 under registration number No. 39517).

40. STCMS functions shall be fulfilled by the Office of Harbor Master using technical facilities of automatic identification system and on VHF channels.

41. 	Ship traffic in the STCMS coverage area shall be regulated by an official of the Office of Harbor Master.

42. 	Communication between the STCMS and the ships in the seaport and approaches thereto shall be maintained on working channel 11 VHF and calling channel 16 VHF, call sign: Okhotsk-32.

Ships heading for the seaport and leaving the seaport shall ask permission from the STCMS for entry/exit on channel 11 VHF, call sign: Okhotsk-32.

43. 	Ships sailing in the waters of the seaport and approaches thereto shall provide the STCMS with the following information by 11 VHF:

on berthing/unberthing;

on commencement and termination of ship’s movement;

on pilot embarkation/disembarkation;

on the entry to the inner harbor of the seaport;

on the ship’s draft;

on the estimated time of approach to the berths and anchorage places of the seaport.

VI. Rules of Ship Stay in the Seaport

## and Anchorage Ground Arrangement

44. 	Ships in the seaport shall ride at anchorages provided in Addendum No. 4 hereto or lie at berths in accordance with the daily schedule approved by the Harbor Master.

45. 	When receiving a storm warning of a wind speed to be increased in excess of 18 meters per second, ships lying at berths or riding at anchor shall leave the seaport, except for the vessels classed by the Russian River Register as having restricted navigation area. Such vessels shall put in the seaport to use it as a shelter in stormy weather.

46. 	Ships still staying in the seaport after receiving a storm warning shall make all reasonable efforts to ensure ship safety at berths in bad weather.

47. 	Ships secured at berths or riding at anchorages of the seaport shall maintain continuous radio watch by 11 VHF.

48. 	Mooring operations in the seaport shall be allowed under:

wind speed of no more than 12 meters per second;

visibility of no less than four cable’s lengths.

49. 	Bare nonselfpropelled ships and ships with defective propeller-rudder system, ship power plant, anchor handling gear, and faulty VHF radio shall only be allowed to ride at anchor if tugboat assistance is available.

50. 	With the wind speed exceeding 12 meters per second and/or wave height exceeding 1.5 meters, the following operations shall be prohibited in the seaport waters:

riding at anchor with other ships secured alongside;

ship-to-ship cargo transfer;

bunkering of ships riding at anchor.

Ships shall cast off the vessels lying at anchor and proceed to anchor at safe places.

51. 	Hauling and shifting of ships in the seaport for a distance in excess of 50 meters shall only be allowed at a wind speed of less than 10 meters per second speed and with pilot and tug assistance available.

Minimum tug assistance for mooring and shifting of ships

of 20 to 35 meters in length makes a single tugboat of no less than 110 kW of power capacity;

of more than 35 meters in length makes two tugboats of no less than 280 kW of total power capacity.

52. 	Ships shall be moored by a mooring crew with the number of people therein depending on the gross registered tonnage of the ship as follows:

ships less than 200 DWT – 2 mooring masters;

ships of 200 to 500 DWT – 4 mooring masters;

ships greater than 500 DWT – 6 mooring masters.

Lead mooring master shall be equipped with a radio to communicate with the ship master.

53. 	Simultaneous mooring at the adjacent berths shall be prohibited.

54. 	Diving operations in the seaport shall be allowed upon authorization of the Harbor Master under the following conditions:

wind speed - no more than 10 meters per second;

seas - not higher than 2 points;

water under the keel of the ship examined - no less than two meters;

visibility - no less than five cable’s lengths;

no cargo handling operations on board the ship.

Ship master shall inform the Harbor Master of the commencement and termination of diving operations.

55. 	Cargo handling operations in the seaport, using portal cranes, crane trucks and ship-borne cargo handling gear shall be allowed at a wind speed of no more than 15 meters per second.

## VII. Rules of Ecological Safety, Including Identification of Shipboard Waste to Be Collected at the Seaport, and Rules of Quarantine Compliance in the Seaport

56. 	This seaport shall not collect oily polluted waters and sewage waters. Garbage shall be collected at the ship master’s request.

57. 	Ships shall be allowed to discharge their segregated ballast within the port limits providing that the ballast has been taken on board at the Sea of Japan or the Sea of Okhotsk at a distance of no less than 50 meters from the nearest shore and in places of no less than 200 meters deep, in witness whereof a corresponding log record has been made.

58. 	For oil loading/unloading and bunkering operations in the seaport, boom defense shall be secured.

In case of oil or petroleum product spills on board a ship or within the seaport water area all handling operations shall be ceased, and crewmen and a berth owner shall take measures for oil or petroleum product spill containment.

59. 	Ships shall immediately report a pollution incident in the water area to the Office of Harbor Master by any means of communication available. The information shall be inclusive of:

the oil spill detection time;

weather conditions (sea condition, wind speed and direction, visibility);

nature of pollution and extent of polluted area;

likely source of pollution;

spill containment measures taken.

Ships shall not be allowed to cross the polluted area. When proceeding close to the oil spill cleanup area, a ship shall slow down to the slowest practical speed to hold the ship on course.

60. 	A ship with a patient having symptoms suspicious for highly infectious disease shall proceed together with the crew, passengers and cargo for antiepidemic measures to quarantine anchorage No. 8 as provided in Addendum No. 4 hereto.

## VIII. Rules to Use Special Communication Facilities within the Seaport Territory

61. 	Ships riding out at berths or in the water area of the seaport shall maintain continuous radio watch by calling channel 11 VHF.

62. 	Radio communication by 11 VHF in the seaport for the purpose other than navigation safety shall not be allowed.

63. 	The Harbor Master shall provide the seafarers with the data on additional communication facilities for information transmission, including telephone numbers.

64. 	Small crafts, sport sailers and pleasure boats in the water area of the seaport shall maintain continuous radio watch by calling channel 11 VHF.

## IX. Data on the Seaport Capabilities to Accommodate Ships

## and on Water Depths in the Seaport and Approaches Thereto

65. 	The seaport accommodates ships up to 110 meters LOA, 18 meters wide with a draft up to 9 meters. The inner harbor shall accommodate ships with a draft up to 3.5 meters.

The data on the seaport capability to accommodate ships and on water area depths in the seaport are provided in Addendum No. 5 hereto.

66. 	Data on depths in the water area of the seaport and approaches thereto, at berths, at the sand bar of Kukhtuy river mouth as well as canal drafts be provided by the Harbor Master to the seafarers on an annual basis and in case of changes therein.

67. 	Upon preparing a berth for berthing (unberthing), any cargo, equipment and other implements located within an area less than five meters wide from the wharf face line shall be removed from the berth.

## X. Data on Hazardous Cargo Handling

68. 	Handling of hazardous cargo of IMO hazard classes 1, 4, 5, 6, 8 and 9 shall be allowed in the seaport.

69. 	Handling of IMO hazard class 1.1 cargo in the seaport shall only be allowed during daylight.

70. 	Handling of hazardous cargo shall be allowed under the following weather conditions:

at a wind speed of no more than 12 meters per second;

at a wave height of no more than 1.5 meters.

XI. Data on Transmission of Information by Masters of the Ships

Staying in the Seaport in Case of Threatened Act of Unlawful

Intervention in the Seaport

71. 	In case of a threatened act of unlawful intervention in the seaport, the master of the ship or the ship security officer shall immediately notify a port facility security officer, a port state control inspection officer on duty, and the Harbor Master thereof using any means of communication available.

72. 	The Harbor Master shall be informed of the port facility security level by the marine terminal operators, security level of the ships staying in the seaport by the ship masters as well as be notified of any change in security levels thereof.

73. 	Any suspicious items or explosive devices found, signs of threatened acts of unlawful intervention identified, ship intruders or attempted intrusion detected, any information on threatened terrorist attacks as well as any violation of the seaport routine or any suspicious strangers in the seaport shall be immediately reported by the masters of the ships staying in the seaport to the Harbor Master, the port facility security officer using VHF channels and any additional means of communication made known to the parties concerned by the Harbor Master.

74. 	Warnings of any threatened acts of unlawful intervention in the seaport and of changes in the security levels of the ships staying in the seaport as well as acknowledgment of receipt of the said warnings shall be given immediately after the circumstances stated in the warnings arise.

XII. Transmission of Navigational, Hydrological and Meteorological

Information to Masters of the Ships Staying in the Seaport

75. 	Hydrometeorological information to the ships staying in the seaport shall be transmitted by 11 VHF.

76. 	The Harbor Master shall transmit urgent nautical and hydrometeorological information as well as storm warnings to the ships at berths or anchorages of the seaport by 11 VHF. When vital messages and storm warnings are received, the ships shall at all times acknowledge receipt of such messages and warnings.

## Addendum No. 1

to the Seaport Regulations

(Cl. 7)

DATA ON THE APPROACHES TO THE SEAPORT

Approaches to the seaport are bounded by straight lines connecting the following points one after another:

1. 59°18'12" N, 143°14'12" E;

2. 59°18'12" N, 143°01'42" E;

3. 59°16'30" N, 143°01'42" E;

4. 59°16'30" N, 143°14'12" E.

## Addendum No. 2

to the Seaport Regulations

(Cl. 13)

DATA ON THE COMPULSORY PILOTAGE AREA

IN THE SEAPORT

The compulsory pilotage area in the seaport comprises:

1) 	seaport waters – an area bounded by the shoreline and lines connecting the following points one after another:

59°20'44,5" N, 143°08'23,0" E;

59°21'19,5" N, 143°11'06,2" E;

59°21'10,3" N, 143°11'15,0" E;

2) 	entry to the lagoon at the mouth of Kukhtuy river located between Okhotskaya Kosa island and the Tungusky spit;

3) 	a portion of the seaport water area south of the entry to the mouth of Kukhtuy river bounded by lines:

from the point at 59°19'30" N, 143°09'00" E northwards to the shoreline;

from the point at 59°19'30" N, 143°09'00" E to the point at 59°20'9" N, 143°10'00" E.

## Addendum No. 3

to the Seaport Regulations

(Cl. 16)

DATA ON VERY HIGH FREQUENCY CHANNELS USED IN THE SEAPORT

| User | VHF channels | Call sign |
| --- | --- | --- |
|  | Calling channel | Working channel |  |
| Port State Control Inspection | 11 | 11 | Okhotsk-32 |
| Ship Traffic Control and Management Service | 16 | 11 | Okhotsk-32 |
| Harbor Master | 11 | 11 | Okhotsk-32 |
| Freight terminal dispatcher | 11 | 11 | Okhotsk-31 |
| Tugboats in mooring | 11 | 13 | Tugboat name: МB-371 or Uelen |
| Pilot | 11 | 13 | Lotsman-Okhotsk |

## Addendum No. 4

to the Seaport Regulations

(Cl. 17, 44, 60)

DATA ON SEAPORT ANCHORAGES

Anchorage No. 1 is bounded by a circle having a radius of 1.5 nautical miles with a center at 59°18'24" N and 143°10' E.

Anchorage No. 2 is bounded by a circle having a radius of 1.5 nautical miles with a center at 59°18'24" N and 143°08' E.

Anchorage No. 3 is bounded by a circle having a radius of 1.5 nautical miles with a center at 59°19' N and 143°10' E.

Anchorage No. 4 is bounded by a circle having a radius of 1.5 nautical miles with a center at 59°19' N and 143°08' E.

Anchorage No. 5 is bounded by a circle having a radius of 1.1 nautical miles with a center at 59°20' N and 143°10' E.

Anchorage No. 6 is bounded by a circle having a radius of 1.1 nautical miles with a center at 59°20' N and 143°11' E.

Anchorage No. 7 is bounded by a circle having a radius of 1.1 nautical miles with a center at 59°20' N and 143°12' E.

Anchorage No. 8 is bounded by a circle having a radius of 1.5 nautical miles with a center at 59°19' N and 143°12' E.

Anchorage No. 9 is bounded by a circle having a radius of 1.1 nautical miles with a center at 59°18'30" N and 143°05' E.

Anchorage No. 10 is bounded by a circle having a radius of 1.1 nautical miles with a center at 59°19' N and 143°05' E.

Anchorage Nos. 1, 2, 9, 10 are intended for ship-to-ship cargo transfer.

Anchorage Nos. 3 and N 4 are intended for ship clearance by port state control authorities and ship-to-ship cargo transfer.

Anchorage Nos. 5, 6, 7 are intended for ships having a draft of no more than 3.0 meters.

Anchorage No. 8 is intended for quarantine stay, for hazardous cargo-carrying ships, and tankers.

## Addendum No. 5

to the Seaport Regulations

(Cl. 18, 65)

DATA ON THE SEAPORT CAPABILITY TO ACCOMMODATE SHIPS

AND ON WATER AREA DEPTHS

| Berth description | Berth location | Specification |
| --- | --- | --- |
|  |  | Berth length (meters) | (Planned) depth at berth (meters) |
| 1 | 2 | 3 | 4 |
| Berth No. 1 | 59°21'06" N and 143°10'58" E | 82.3 | 3.14 |
| Berth No. 2 | 59°21'03" N and 143°10'54" E | 190.0 | 3.86 |
| Berth No. 3 | 59°21'03" N and 143°10'46" E | 99.0 | 3.86 |
| Berth No. 4 | 59°21'02" N and 143°10'39" E | 125.0 | 3.86 |
| Berth No. 5 | 59°21'01" N and 143°10'35" E | 55.7 | 3.14 / 4.14 |